Scientific-industrial group (J.S.C. «Nezhyn Mechanical Factory, Ukrainian State University of food technologies and «Intermash» company) is the leading one in the branch of manufacturing the equipment for food industry in Ukraine as well in the countries of the Commonwealth of Independent Countries.

This machine is designed in accordance with the modern technologies. Pancake makers MBN-800 are accepted as meeting high quality standards not only by our customers in the countries of the Commonwealth of Independent States but also in many counties abroad.

- FUNCTION.

MBN- 800 pancake maker is designed to make small pancakes of the folded-leaf type to be filled with meat, curds or jam and for use at large public catering enterprises.

- MACHINE PARTS.

- Mainframe.   2. Staff feeder.  3. The foundation of the column.  4. Stuff hopper. 5. Dough tank.  6. Folding conveyer. 7. Block of electric equipment. 8. Storage table. 9. Trough for dough. 10. Drum. 11. Frame nose.

- TECHNICAL DATA.

| Productivity, pcs. per hour, min | 800 |
| --- | --- |
| Nominal dimension of dough sheet, mm | 220 х 280 |
| Weight of dough sheet, gr. | 45 |
| Quantity of staff types | 3 |
| Nominal dimension of the pancake, mm | 70 х 90 |
| Nominal pancake weight, gr. With meat staff With curds staff With jam staff | 75 75 65 |
| Staff weight, gr. meat curds jam | 30 30 20 |
| Dough tank capacity, dm3, min | 34 |
| Stuffing hopper capacity, dm3, min | 15 |
| Electric power, kW Voltage, V Frequency, Hertz | 18,2 380 50 |
| Electric power consumption, kW/hr, max | 13,2 |
| Water consumption, m3/hr, max | 0,4 |
| Personnel, men/shift | 2 |
| Dimensions, mm, max length width height | 2100 1100 1700 |
| Weight, kg, max | 600 |

With best regards,

Golofastov Yuriy Vladimirovich.

Mob.tel: + 38 067-811-87-96.

E-mail: fishmuka@yandex.ru

www.unitsforfishmeal.narod.ru

J.S.C. «Nezhyn Mechanical Factory»

Ukraine